## Slide 1: Scanning ARM Cloud Radar (SACR)

## Slide 2: 3D clouds scan strategies
CW-RHI:
A sequence of 0-180° elevation scans at constant azimuth perpendicular to cloud-level mean wind direction
Scan rate: 9°/sec
Sensitivity at 1km: -50dBZ
CW-RHI mode

## Slide 3: 3D clouds
Discussion points:
Does 3-D vertical Doppler velocity provide more information than the curtain profiles from the zenith radars?
Our results suggest:
3D clouds do provide an insight on cloud scale dynamic organization
Eddy strength, shape, tilt, orientation with respect to wind, distribution across range, penetration depth
Future work:
Use Gridded SACR data to study/quantify cloud anisotropy and in-cloud turbulence
Constant height
Gridded vertical Doppler velocity
3-D Clouds

## Slide 4: SACR scan strategies
HS-RHI mode:
RHI scan from 0-180° elevation at fixed azimuth
Repeated every 30° azimuth to cover a 360° sector
Completed in 3 min.
Cycle repeated every 30 min
Scientific objective: Document horizontal wind speed and direction
BL-RHI mode:
RHI scans from 4-80°elevation at fixed azimuth
Repeated every 3° azimuth to cover a 60° sector
Completed in 5 min
Cycle repeated 4 consecutive times
Scientific objective: 3-D cloud life cycle (4-D)
BL-RHI mode
Height (km)
Azimuthal Range (km)
Range (km)
HS-RHI mode

## Slide 5: Gridding Validation
Two things need to be validated
  Cloud fraction
  Are we creating fictitious clouds?
  The values inside the grid
  Are we interpolating correctly?
  Currently there are no other instruments located underneath the region observed by the SACR so no synergistic validation is possible.
  We propose to install a Total Sky Imager below the region to provide cloud fraction comparisons
  We also propose to move a vertically pointing radar below the region to provide point measurement comparison
We create a composite of the processed data at a constant height to roughly compare with the gridded data.
  Mathematically, interpolation is valid and has been used for weather radar gridding.
  Visually it also seems accurate.
Gridded Reflectivity
Processed Reflectivity composite

## Slide 6: Gridding Visualization tool
3-D visualization tools are not readily available for this type of dataset
3-D visualization helps interpreting observations
Display semi-transparent iso-surfaces at a 2dBZ Reflectivity interval
Case study
Continental region
Fall (September)
Stratocumulus cloud
2 layer
Low-level (first layer around 800m second layer around 4km)
No heavy precipitation (No precipitation reaching the ground
Drizzling (Reflectivity above -20dBZ)
3-D Gridded Reflectivity

## Slide 7: Life cycle analysis Drizzle
Reflectivity evolution at 875m over 24 minutes
Stratocumulus cloud containing pockets of drizzle
This cloud is in it’s decaying phase
A few questions we can investigate:
  Is drizzle responsible for the decay of this cloud?
    Is drizzle area correlated with cloud fraction?
    Is drizzle volume correlated with cloud volume?
    Are drizzle pockets more likely to break up?
    Is drizzle growing or weakening?
Requires global statistics
Requires tracking

## Slide 8: Life cycle analysis Future work
Next step will be to remove the mean flow from the observed Doppler Velocity to observe the internal circulations within stratocumulus clouds
Then calculate a new wind vector for advection
Doppler velocity at 875m
Doppler velocity at 875m

## Slide 9: References
Lamer, K., Tatarevic, A., Jo, I., and Kollias, P.: Evaluation of gridded scanning ARM cloud radar reflectivity observations and vertical doppler velocity retrievals, Atmos. Meas. Tech., 7, 1089-1103, doi:10.5194/amt-7-1089-2014, 2014.
Kollias, Pavlos, Nitin Bharadwaj, Kevin Widener, Ieng Jo, Karen Johnson, 2014: Scanning ARM Cloud Radars. Part I: Operational Sampling Strategies. J. Atmos. Oceanic Technol., 31, 569–582
Kollias, Pavlos, and Coauthors, 2014: Scanning ARM Cloud Radars. Part II: Data Quality Control and Processing. J. Atmos. Oceanic Technol., 31, 583–598. doi: http://dx.doi.org/10.1175/JTECH-D-13-00045.1